## Slide 1: Mechanics and machines
Project

## Slide 2: Possible projects

## Slide 3: Workflow
Choose Project
Kinematics
Dynamics
CAD + CAE
modeling
Hardware Assembly

## Slide 4: Best projects will be published
It is the reason why do you need to write reports nicely Example: paper (recommend to get acquainted)

## Slide 5: Choose Project: Guideline
Come up with possible projects and fill the form
Discuss with instructor
Present a presentation (7 min, strict). It should contain slides about:
  What is the Idea To show up your project, what the problem you want to solve or what was your inspiration.
  Challenges: what are the most complicated parts. In some projects it can be to invent a design, in some - dynamics. Show your understanding.
  Proposed constraints and boundaries: Min and Max dimensions, weight The goal is to show that you understood how the final project should look like
  Preliminary list of components and mechanisms: It should be the list contains common mechanisms (crank shafts, worm gears), specific components (springs), materials (metal, plastic). Explain why do you need it.
  Goals of kinematics, dynamics, durability analysis: Exp: I need to generate traj. of an end-effector. I interested in positions for kinematics. My robot moves slowly, I don’t need dynamics, only static analysis. It should survive after 20 kg load.

## Slide 6: Kinematics: Guideline
To understand what do you need to achieve. Find only positions, or you need positions and velocities, may you need to find a gear ratio? Do you need to generate a trajectory?
Draw a kinematics scheme Tip: sometimes it’s easier to make in CAD, to play with it and afterwards – code it (as you did in TM).
Solve kinematics problem For some cases - to write equations and check them by drawing plots or making a simulation (like in TM). If you need to generate a trajectory, you need to write fitness function, choose method, parameters and variables. Estimate obtained results.
Write a report Tip: assume that you are writing it for the guy, who haven’t seen your project. It means, it’s better to explain the goals of each step like - why do you finding kinematics and so on.

## Slide 7: Dynamics: Guideline
To understand what do you need to achieve. Find torques, motion? Make only static analysis?
Make force analysis You need to get what forces are important. Maybe you have to consider friction or not. And so on
Solve dynamics problem You should do it using both simulation in NX and by coding. For making a simulation in NX you have to make very simple CAD model of your mechanism (without screws, etc)
Write a report Tip: assume that you are writing it for the guy, who haven’t seen your project. It means, it’s better to explain the goals of each step like - why do you finding dynamics and so on.

## Slide 8: CAD + CAE modeling: Guideline
Based on kinematics, dynamics make a CAD model Tip: don’t forget to add screws. You should use naming convention.
Using NX estimate durability If you get that something wrong, return to previous steps (CAD or even kinematics)
To show your solution to classmates It might help you to reduce amount of mistakes when you start to assemble and print details.
Write a report Emphasise on the reasons why did you apply X force on your model, how it should work in terms of loads, why did you choose such type of analysis.

## Slide 9: Hardware assembly: Guideline
Buy, find details Don’t forget that the shipping needs some time. It’s not the reason for failing!
Print details You can ask your friends or fellows in lab or garage
Assemble a mechanism Good luck)

## Slide 10: Final presentation: Guideline
Prepare CAD model render
Prepare slides (10 min, strict)
  1) 1-4 slides: Explain your original idea
  2) How it transforms during the semester (if)
  3) Kinematics
  a) 1-2 slides : proposal - what did you try to find, the purpose
  b) 1-2 slides: solution (video if exists) (without formulas)
  4) Dynamics
  a) 1-2 slides : proposal - what did you try to find, the purpose
  b) 1-2 slides: solution coding (video if exists) (without formulas)
  c) 1-2 slides: solution NX
  d) 1 slides: compare solutions. Justify results
  5) CAE: 1-3 slides: proposal, strain diagram
  6) Render
  7) Video of working mechanism (due the reason, that in a big audience, not everyone will see the mechanism)
  8) 1-2 slides: What did you learn from the project and the course
  9) What would you do in other way if you had such project again

## Slide 11: Best projects: Guideline
Together we are choosing the appropriate journal/conference.
Rewriting your report based on needed template
Submit it
…
Profit! You have your new awesome scientific article

## Slide 12: Deserve “A” grade!
– Oleg Bulichev